### R1 Configuration
enable
configure terminal
hostname R1

interface FastEthernet0/0
 ip address 192.168.10.49 255.255.255.248
 no shutdown

interface FastEthernet0/1
 ip address 192.168.10.26 255.255.255.248
 no shutdown

router ospf 1
 router-id 1.1.1.1
 network 192.168.10.48 0.0.0.7 area 0
 network 192.168.10.24 0.0.0.7 area 0

end
write memory

### R3 Configuration
enable
configure terminal
hostname R3

interface FastEthernet0/0
 ip address 192.168.10.34 255.255.255.248
 no shutdown

interface FastEthernet0/1
 description Connection to Network-6 (PC2, PC3)
 ip address 192.168.10.41 255.255.255.248
 no shutdown

router ospf 1
 router-id 3.3.3.3
 network 192.168.10.40 0.0.0.7 area 0
 network 192.168.10.32 0.0.0.7 area 0

end
write memory

### R4 Configuration
enable
configure terminal
hostname R4

interface FastEthernet0/0
 ip address 192.168.10.35 255.255.255.248
 no shutdown

interface FastEthernet0/1
 ip address 192.168.10.57 255.255.255.248
 no shutdown

router eigrp 100
 network 192.168.10.56 0.0.0.3
 network 192.168.10.32 0.0.0.7
 auto-summary

router ospf 1
 router-id 4.4.4.4
 network 192.168.10.32 0.0.0.7 area 0

end
write memory

### R5 Configuration
enable
configure terminal
hostname R5

interface FastEthernet0/0
 ip address 192.168.10.27 255.255.255.248
 no shutdown

interface FastEthernet0/1
 ip address 192.168.10.33 255.255.255.248
 no shutdown

router eigrp 100
 network 192.168.10.32 0.0.0.7
 auto-summary

router ospf 1
  router-id 5.5.5.5
  network 192.168.10.24 0.0.0.3 area 0
  network 192.168.10.32 0.0.0.3 area 0

end
write memory

### R6 Configuration

enable
configure terminal
hostname R6

interface FastEthernet0/0
 ip address 192.168.10.25 255.255.255.248
 no shutdown

interface FastEthernet0/1
 ip address 192.168.10.19 255.255.255.248
 no shutdown

router ospf 1
  router-id 6.6.6.6
  network 192.168.10.24 0.0.0.3 area 0

router eigrp 100
 network 192.168.10.16 0.0.0.7
 auto-summary

end
write memory

### R7 Configuration

enable
configure terminal
hostname R7

interface FastEthernet0/0
 ip address 192.168.10.1 255.255.255.248
 no shutdown

interface FastEthernet0/1
 description Connection to Network-1 (Server-4)
 ip address 192.168.10.17 255.255.255.248
 no shutdown

router bgp 200
 bgp router-id 7.7.7.7
 neighbor 192.168.10.58 remote-as 100
 network 192.168.10.0 mask 255.255.255.248
 network 192.168.10.16 mask 255.255.255.248
!
end
write memory

R8 Configuration
enable
configure terminal
hostname R8

interface FastEthernet0/0
 ip address 192.168.10.18 255.255.255.248
 no shutdown

interface FastEthernet0/1
 ip address 192.168.10.9 255.255.255.248
 no shutdown

router eigrp 100
 network 192.168.10.8 0.0.0.7
 network 192.168.10.16 0.0.0.7
 auto-summary

end
write memory