### Network Topology & IP Addressing Plan

Device	Interface	Ip Address	Subnet Mask	Connected Network	Server IP
Router3	Fa0/0 (LAN)	192.168.1.1	255.255.255.0	192.168.1.0/24	DNS Server: 192.168.1.2
	Se0/0/0 (to R4)	10.0.0.1	255.255.0.0	10.0.0.0/16	-
	Se0/1/0 (to R5)	10.2.0.1	255.255.0.0	10.2.0.0/16	-
Router4	Fa0/1 (LAN)	192.168.2.1	255.255.255.0	192.168.2.0/24	HTTP Server: 192.168.2.2
	Se0/0/0 (to R3)	10.0.0.2	255.255.0.0	10.0.0.0/16	-
	Se0/1/0 (to R5)	10.1.0.1	255.255.0.0	10.1.0.0/16	-
Router5	Fa0/0 (LAN)	192.168.3.1	255.255.255.0	192.168.3.0/24	FTP Server: 192.168.3.2
	Se0/0/0 (to R4)	10.1.0.2	255.255.0.0	10.1.0.0/16	-
	Se0/1/0 (to R3)	10.2.0.2	255.255.0.0	10.2.0.0/16	-

### Router3 Routing Table

Destination Network	Subnet Mask	Next Hop	Interface	Notes
192.168.1.0	255.255.255.0	Direct	Fa0/0	Directly connected LAN (DNS server at 192.168.1.2)
10.0.0.0	255.255.0.0	Direct	Se0/0/0	P2P link to Router4
10.2.0.0	255.255.0.0	Direct	Se0/1/0	P2P link to Router5
192.168.2.0	255.255.255.0	10.0.0.2	Se0/0/0	RIP via Router4 (HTTP server at 192.168.2.2)
192.168.3.0	255.255.255.0	10.2.0.2	Se0/1/0	RIP via Router5 (FTP server at 192.168.3.2)
10.1.0.0	255.255.0.0	10.0.0.2	Se0/0/0	RIP via Router4 (equal-cost path also exists via Router5, but RIP uses first path)

### Router4 Routing Table

Destination Network	Subnet Mask	Next Hop	Interface	Notes
192.168.2.0	255.255.255.0	Direct	Fa0/1	Directly connected LAN (HTTP server at 192.168.2.2)
10.0.0.0	255.255.0.0	Direct	Se0/0/0	P2P link to Router3
10.1.0.0	255.255.0.0	Direct	Se0/1/0	P2P link to Router5
192.168.1.0	255.255.255.0	10.0.0.1	Se0/0/0	RIP via Router3 (DNS server at 192.168.1.2)
192.168.3.0	255.255.255.0	10.1.0.2	Se0/1/0	RIP via Router5 (FTP server at 192.168.3.2)
10.2.0.0	255.255.0.0	10.0.0.1	Se0/0/0	RIP via Router3 (equal-cost path also exists via Router5)

### Router5 Routing Table

Destination Network	Subnet Mask	Next Hop	Interface	Notes
192.168.3.0	255.255.255.0	Direct	Fa0/0	Directly connected LAN (FTP server at 192.168.3.2)
10.1.0.0	255.255.0.0	Direct	Se0/0/0	P2P link to Router4
10.2.0.0	255.255.0.0	Direct	Se0/1/0	P2P link to Router3
192.168.1.0	255.255.255.0	10.2.0.1	Se0/1/0	RIP via Router3 (DNS server at 192.168.1.2)
192.168.2.0	255.255.255.0	10.1.0.1	Se0/0/0	RIP via Router4 (HTTP server at 192.168.2.2)
10.0.0.0	255.255.0.0	10.1.0.1	Se0/0/0	RIP via Router4 (equal-cost path also exists via Router3)

Configurations:

Router3 Configuration:

enable
configure terminal
interface FastEthernet0/0
ip address 192.168.1.1 255.255.255.0
no shutdown
interface Serial0/0/0
ip address 10.0.0.1 255.255.0.0
no shutdown
interface Serial0/1/0
ip address 10.2.0.1 255.255.0.0
no shutdown
router rip
version 2
no auto-summary
network 10.0.0.0
network 192.168.1.0
end
write memory

Router4 Configuration:

enable
configure terminal
interface FastEthernet0/1
ip address 192.168.2.1 255.255.255.0
no shutdown
interface Serial0/0/0
ip address 10.0.0.2 255.255.0.0
no shutdown
interface Serial0/1/0
ip address 10.1.0.1 255.255.0.0
no shutdown
router rip
version 2
no auto-summary
network 10.0.0.0
network 192.168.2.0
end
write memory

Router5 Configuration:

enable
configure terminal
interface FastEthernet0/0
ip address 192.168.3.1 255.255.255.0
no shutdown
interface Serial0/0/0
ip address 10.1.0.2 255.255.0.0
no shutdown
interface Serial0/1/0
ip address 10.2.0.2 255.255.0.0
no shutdown

router rip
version 2
no auto-summary
network 10.0.0.0
network 192.168.3.0
end
write memory